## Slide 1: X-Men: The Last Stand
John McKay, Nathan Donaldson, Clint Wilkinson, Keith Madsen

## Slide 2: Overview
Intro and ALU Design - (John McKay)
Register Design and Integration with ALU - (Nathan Donaldson)
Memory Access Interface - (Clint Wilkinson)
Mechanical Crane Application - (Keith Madsen)

## Slide 3: ALU Design
16 bit ALU
CR 16 Instruction Set
Opcode encoding is:
  (bits 7-4) opcode
  (bits 3-0) Opcode extension or Immediate
  This will change with controller

## Slide 4: ALU Design
Use mux to put immediates on input A
Flags are stored in a flag register
Cin comes from the flag register

## Slide 5: ALU Design
Current Opcode Instructions
Adds
Subtracts
Compares
Logical Operators
Shifts
Not
WAIT / NOP
Moves
Things to add in the future
LOAD
STORE
Jump/Branch
Sign extend immediates
Controller to set the opcode/immediate

## Slide 6: ALU Testing
Tested each opcode using corner cases
Exhaustive testing using Random simulator tests
Miter Test
Made a display module for the 7 seg-display
Synthesized tests to the FPGA and displayed results on 7 seg-display

## Slide 7
ALU, Register File, Control Signals
Read_A and IMM_BUS sent to MUX
Read_Imm controls said MUX
Write controls enable signal on each register
Clk, reset, READ_B

## Slide 8
Inputs: Flags(from ALU), clk, ALU Bus input, reset, register enable.
Cin flag loops back to ALU
Other flags will be used later.
R9-R15 Temp
R2-R8 Save
R1 Stack Pointer
R0 Return Address
FP, others?

## Slide 9
Buffer is filled with tristate buffers.
This buffer is MUXed with an immediate bus.
BusB does not have MUX.

## Slide 10: Testing
Fibonacci Sequence
R0 + R1 -> R1 -> R2
R1 + R0 -> R0 -> R3
R0 + R1 -> R1 -> R4
………

## Slide 11: Memory
Characteristics
Dual Port / Write First
32 Blocks / 1024 Words per block
16 bit Words
Divisions
  Instructions
  Data
  VGA/Sound

## Slide 12: Port Assignments
Port A
Processor use only
Port B
VGA
Sound
Limit Switchs

## Slide 13: Memory Testing
Individual Reads and Writes
Simultaneous Reads and Writes with both ports.
Simultaneous Reads and Writes using previously written values.

## Slide 14
Problems
Read First vs. Write First
Enable Pulse vs. Direct Clock Divider

## Slide 16: Mechanical Crane A.K.A The Fishing Game
Motorized Game
Compass Movements
Z Axis Not Shown
Limit Switches
NES/SNES Controlled
Pick Up Items or Fish
N
S
E
W
Limit Switch
Limit Switch

## Slide 18: Future Considerations
Motorized Turntable with Variable Speed
Electro Magnet
Sound
Auto Scoring Bin
Cost

## Slide 19: Summary
ALU Discussion
Register File and ALU Combination
Memory
Project Direction

## Slide 20: Questions?